## Slide 1: TSDuck
an extensible toolkit for
MPEG/DVB transport streams
Version 3.0 – June 2017

## Slide 2: Agenda
TSDuck overview
TS utilities
Transport stream processor
Sample scripts
Extending TSDuck
Using TSDuck as an MPEG/DVB library for C++

## Slide 3: TSDuck overview
Process ISO/IEC 13818-1 transport streams
Set of low-level utilities
  extensible through plugins
« Batch & Bash » oriented
  command-line only, no fancy GUI
  one utility or plugin = one elementary function
  can be combined in any order
Written in C++
  reusable and extensible code
Available on Linux, Windows and macOS

## Slide 4: TSDuck sample usages
TS acquisition (satellite, terrestrial, IP, etc.)
TS analysis
Transmodulation
Injection of PSI / SI
TS packets carousel generation
  Packetization of SSU, etc.
Test bed for CAS or STB
  Injection of test cases
  DVB Scrambling and DVB SimulCrypt support
Any combination of the above and more…

## Slide 5: TSDuck availability
Open source code
  https://github.com/lelegard/tsduck
BSD 2-clause license
Binary installers
  for Windows, Fedora, Ubuntu

## Slide 6: TSDuck documentation
User’s Guide
  Utilities reference
  TSP plugins reference
  Sample usages
Programmer’s Reference
  Generated by Doxygen from source code
  TSDuck C++ common code reference
  Writing tsp plugins guidelines

## Slide 7: the command line utilities summary
TS Utilities

## Slide 8: TS utilities : data & devices
Transport stream file
  Raw binary file, sequence of 188-byte TS packets
    use tsresync to convert 204-byte packets or corrupted files
  By default, use standard input & output
    can use pipes from / to any DVB source
PSI / SI file
  Raw binary file, sequence of sections
Specialized hardware
  DVB-S, DVB-T, DVB-C tuners (cheap CE devices)
  Dektec modulators and ASI input / output (PCI, USB)
  Smartcards
  On Linux and Windows but not macOS

## Slide 9: TS utilities summary (1/4)
Transport stream processor
  tsp : processing framework using plugins
TS analysis
  tsanalyze : synthetic report
    TS structure, services, PID’s
    can also produce a « normalized » output for automatic processing
  tspsi : detailed analysis of main PSI / SI tables in TS
    PAT, CAT, PMT, SDT, NIT, BAT
  tsbitrate : evaluate original bitrate from PCR’s
  tsdate : extract date & time information

## Slide 10: TS utilities summary (2/4)
Transport packet analysis
  tsdump : dump and analyze transport packets
TS files recovery
  tsresync : fix corrupted capture files
  tsftrunc : truncate TS files
  tsfixcc : fix continuity counters

## Slide 11: TS utilities summary (3/4)
PSI / SI tables
  tstables : extract sections & tables from TS
    either binary or textual analysis
  tstabdump : textual analysis of binary table files
  tspacketize : generate TS packets from tables
    sample usage : delivery of packet carousel for tables
  tsgentab : generate specific tables using plugins
    each plugin typically generates one table
    add new plugins when new tables are needed

## Slide 12: TS utilities summary (4/4)
Various DVB hardware support
  tsdektec : control Dektec devices
  tslsdvb : list DVB receiver devices
  tsscan : scan frequencies in a DVB network
  tsterinfo : compute various DVB-T information
  tssmartcard : list or reset smartcard reader devices

## Slide 13: the transport steam processor
TSP

## Slide 14: TSP overview
Transport stream processing framework
  Combination of elementary processing using plugins
  One input plugin
    receive a TS from various sources
  Any number of packet processing plugins
    perform transformations on TS packets
    may remove packets
    may NOT add packets
  One output plugin
    send the resulting TS to various destinations

## Slide 15: TSP processing overview
tsp process
tsp executable
packet processing plugin 2
packet processing plugin 1
packet processing plugin 3
input plugin
output plugin
input TS
output TS

## Slide 16: TSP plugins
Each tsp plugin is a shareable library
  .so file on Linux and macOS
  .dll file on Windows
File naming
  Plugin named foo in file tsplugin_foo.so (or .dll)
  Same directory as tsp executable
General command line syntax
  tsp [tsp-options] \ [-I input-name [input-options]] \ [-P processor-name [processor-options]] ... \ [-O output-name [output-options]]

## Slide 17: TSP examples (1/4)
TS acquisition
  tsp –I dvb –-uhf 21 \ -P until –-seconds 20 \ -O file capture.ts
Display the PMT of a selected service
  tsp –I dvb –-uhf 35 \ -P zap france2 \ -P sifilter –-pmt \ -P tables –-max 1 \ -O drop
capture DVB-T stream from UHF channel 21
pass packets during 20 seconds, then stop
save TS to file capture.ts
extract service « France 2 », rebuild SPTS
extract PID containing PMT
display one table, then stop
drop output packet (don’t care)

## Slide 18: Thank you