## Slide 1: TSDuck
an extensible toolkit for
MPEG/DVB transport streams
TSDuck Version 3.9

## Slide 2: Agenda
TSDuck overview
TS utilities
Transport stream processor
XML table compiler
Extending TSDuck
Using TSDuck as an MPEG/DVB library for C++

## Slide 3: TSDuck overview
Process ISO/IEC 13818-1 transport streams
Set of low-level utilities
  extensible through plugins
« Batch & Bash » oriented
  command-line only, no fancy GUI
  one utility or plugin = one elementary function
  can be combined in any order
Written in C++
  reusable and extensible code
Available on Linux, Windows and macOS

## Slide 4: TSDuck sample usages (1/2)
TS acquisition (satellite, terrestrial, IP, etc.)
TS analysis
Transmodulation
Analysis, edition, injection of PSI / SI
  using and editing PSI/SI in XML format
TS packets carousel generation
  packetization of SSU, etc.
MPE injection and extraction (Multi-Protocol Encapsulation)

## Slide 5: TSDuck sample usages (2/2)
Test bed for CAS or STB
  injection of test cases
  DVB Scrambling and DVB SimulCrypt support
Extraction of specific streams
  T2-MI (DVB-T2 Modulator Interface)
  PLP’s (Physical Layer Pipe)
  Teletext subtitles
  SCTE 35 splicing
Any combination of the above and more…

## Slide 6: TSDuck availability
Web site
  https://tsduck.github.io/
Open-source code
    https://github.com/tsduck/tsduck
BSD license
  liberal, no GPL-like contamination
Installation
  pre-built binary installers for Windows, Fedora, Ubuntu, Raspbian
  using Homebrew on macOS

## Slide 7: TSDuck documentation
User’s Guide
    https://github.com/tsduck/tsduck/raw/master/doc/tsduck.pdf
  utilities reference
  tsp plugins reference
  sample usages
Programmer’s Reference
    https://tsduck.github.io/doxy/html/
  generated by Doxygen from source code
  C++ common code reference
  writing tsp plugins guidelines

## Slide 8: the command line utilities summary
TS Utilities

## Slide 9: TS utilities : data & devices
Transport stream file
  raw binary file, sequence of 188-byte TS packets
    use tsresync to convert 204-byte packets or corrupted files
  by default, use standard input & output
    can use pipes from / to any DVB source
PSI / SI file
  raw binary file, sequence of sections
Specialized hardware
  DVB-S, DVB-T, DVB-C tuners (cheap CE devices)
  Dektec modulators and ASI input / output (PCI, USB)
  smartcards
  on Linux and Windows but not macOS

## Slide 10: TS utilities summary (1/4)
Transport stream processor
  tsp : processing framework using plugins
TS analysis
  tsanalyze : synthetic report
    TS structure, services, PID’s
    can also produce a « normalized » output for automatic processing
  tspsi : detailed analysis of main PSI / SI tables in TS
    PAT, CAT, PMT, SDT, NIT, BAT
  tsbitrate : evaluate original bitrate from PCR’s
  tsdate : extract date & time information

## Slide 11: TS utilities summary (2/4)
Transport packet analysis
  tsdump : dump and analyze transport packets
TS files recovery
  tsresync : fix corrupted capture files
  tsftrunc : truncate TS files
  tsfixcc : fix continuity counters

## Slide 12: TS utilities summary (3/4)
PSI / SI tables
  tstables : extract sections & tables from TS
    either binary or textual analysis
  tstabdump : textual analysis of binary table files
  tspacketize : generate TS packets from tables
    sample usage : delivery of packet carousel for tables
  tstabcomp : table compiler from XML source files
    also a decompiler which generates XML from captured binary tables

## Slide 13: TS utilities summary (4/4)
Various DVB hardware support
  tsdektec : control Dektec devices
  tslsdvb : list DVB receiver devices
  tsscan : scan frequencies in a DVB network
  tsterinfo : compute various DVB-T information
  tssmartcard : list or reset smartcard reader devices

## Slide 14: the transport stream processor
TSP

## Slide 15: TSP overview
Transport stream processing framework
  Combination of elementary processing using plugins
  One input plugin
    receive a TS from various sources
  Any number of packet processing plugins
    perform transformations on TS packets
    may remove packets
    may NOT add packets
  One output plugin
    send the resulting TS to various destinations

## Slide 16: TSP processing overview
tsp process
tsp executable
packet processing plugin 2
packet processing plugin 1
packet processing plugin 3
input plugin
output plugin
input TS
output TS

## Slide 17: TSP plugins
Each tsp plugin is a shareable library
  .so file on Linux and macOS
  .dll file on Windows
File naming
  plugin named foo in file tsplugin_foo.so (or .dll)
  same directory as tsp executable
General command line syntax
  tsp [tsp-options] [-I input-name [input-options]] [-P processor-name [processor-options]] ... [-O output-name [output-options]]

## Slide 18: TSP examples (1/5)
TS acquisition
  tsp –I dvb –-uhf 21 -P until –-seconds 20 -O file capture.ts
Display the PMT of a selected service
  tsp –I dvb –-uhf 35 -P zap france2 -P sifilter –-pmt -P tables –-max 1 -O drop
capture DVB-T stream from UHF channel 21
pass packets during 20 seconds, then stop
save TS to file capture.ts
extract service « France 2 », rebuild SPTS
extract PID containing PMT
display one table, then stop
drop output packet (don’t care)

## Slide 19: TSP examples (2/5)
Transmodulation of a service over IP multicast
  tsp –I dvb –-uhf 35 -P zap france2 –-audio fra -O ip 224.10.11.12:1000
On-the-fly replacement of a PSI / SI table
  tsp -I dvb --uhf 24 -P inject nit.bin --pid 16 --replace –-stuffing -O dektec --uhf 24 --convolution 2/3 --guard 1/32
extract service « France 2 », keeping only one audio track
broadcast resulting SPTS to multicast IP address:port
replace content of PID 16 with table from binary file
send modified TS to a Dektec DVB-T modulator on same frequency

## Slide 20: TSP examples (3/5)
Conditional Access System test bed
  example using French DVB-T network
Linux or Windows computer
ECMG
EMMG
STB
UHF
coupler
UHF
antenna
MUX: R1, R2, R3, R4, R5, R6
MUX: R9
tsp
DVB-T
tuner
Dektec
DTA-110T
modulator

## Slide 21: TSP examples (4/5)
Conditional Access System test bed (continued)
  tsp -I dvb -u $UHF_INPUT
  -P tsrename -t 9 -a
  -P svrename direct8 -i 0x0901 -l 41 -n "Direct 8 Test"
  -P svrename bfmtv -i 0x0903 -l 42 -n "BFM TV Test"
  -P svrename 'i>tele' -i 0x0904 -l 43 -n "i>TELE Test"
  -P svrename virgin17 -i 0x0905 -l 44 -n "Virgin 17 Test"
  -P svrename gulli -i 0x0906 -l 45 -n "Gulli Test"
  -P svrename france4 -i 0x0907 -l 46 -n "France 4 Test"
  -P svrename 0x02FF -i 0x09FF
  -P scrambler GulliTest -e $ECMG -s $SUPER_CAS_ID
  -p $PMT_CADESC_PRIVATE -a $AC
  -b $ECM_BITRATE --pid $ECM_PID
  -P cat -c -a $CAS_ID/$EMM_PID/$CAT_CADESC_PRIVATE
  -P datainject -r -s $MUX_SERVER_PORT
  -b $EMM_MAX_BITRATE -p $EMM_PID
  -O dektec -u $UHF_OUTPUT --convolution 2/3 --guard 1/32

## Slide 22: TSP examples (5/5)
MPE injection and extraction
Media Server
Network 1
Linux or Windows
DVB
tuner
Linux or Windows
tsp
Dektec modulator
STB
STB
Multicast to
224.250.250.1 : 9000
Network 2
STB
STB
Multicast to
230.2.3.4 : 7000
STB
MPE encapsulation
inside existing TS
DVB
tuner
tsp
Modified destination
in UDP/IP datagrams:
230.2.3.4 : 7000

## Slide 23: TSP input & output plugins
Input plugins
  null : null packet generator
  file : binary TS file
  dektec : Dektec ASI device
  dvb : DVB-S, DVB-T, DVB-C receiver devices
  ip : UDP/IP (unicast or multicast)
Output plugins
  drop : drop packets
  file : binary TS file
  dektec : Dektec ASI or modulator device
  ip : UDP/IP (unicast or multicast)

## Slide 24: TSP processing plugins
TS transformations
  PID or packet filtering, PSI/SI transformation or injection, service extraction, time regulation, etc.
TS analysis and monitoring
  TS analysis, PSI/SI extraction, PID, bitrate monitoring, ECM or EMM monitoring, etc.
TS scrambling & descrambling
  DVB SimulCrypt support for ECM / EMM injection
Any other processing you wish to develop…
  50 packet processing plugins available today

## Slide 25: the PSI / SI table compiler
tstabcomp

## Slide 26: Compiling PSI/SI tables
Input source files
  describe PSI/SI tables in text files
  XML format
Output binary files
  concatenated list of sections
  same format as used by other tools and plugins
Reverse operation (decompilation) also available
  input: binary sections file
  output: XML file

## Slide 27: Sample XML source file
<?xml version="1.0" encoding="UTF-8"?>
<tsduck>
<PAT version="8" transport_stream_id="0x0012" network_PID="0x0010">
<service service_id="0x0001" program_map_PID="0x1234"/>
<service service_id="0x0002" program_map_PID="0x0678"/>
</PAT>
<PMT version="4" service_id="0x0456" PCR_PID="0x1234">
<CA_descriptor CA_system_id="0x0777" CA_PID="0x0251"/>
<component elementary_PID="0x0567" stream_type="0x12">
<ISO_639_language_descriptor>
<language code="fre" audio_type="0x45"/>
<language code="deu" audio_type="0x78"/>
</ISO_639_language_descriptor>
</component>
</PMT>
</tsduck>
Reference format in user’s guide

## Slide 28: Typical application: manual table modification
Tables can be used in XML or binary format anywhere
Capture a table from a stream directly in XML format
    tsp -I dvb ... \
    -P tables --pid 16 --tid 0x40 --max 1 --xml nit.xml \
    -O drop
Manually edit the XML file with a text editor
Inject the updated XML table in the stream
    tsp -I dvb ... -P inject nit.xml --pid 16 ... -O dektec ...

## Slide 29: C++ transport stream programming
Extending TSDuck

## Slide 30: Extending TSDuck
TSDuck is extensible
  Source code provided
      git clone https://github.com/tsduck/tsduck.git
  Common API for Linux, Windows and macOS
    DVB tuners and Dektec cards are not supported on macOS
  Programmer’s guide
    Doxygen-generated, see https://tsduck.github.io/
You can modify it yourself !

## Slide 31: Why extending TSDuck ?
Identify your needs
Try to find a solution using existing TSDuck
  review utilities and plugins
Try to extend an existing utility or plugin
  add new options
  add features, don’t modify existing behavior
  remain upward compatible
Develop your own plugin
  it is quite simple, really
Send your code back to TSDuck maintainer
  so that everyone can benefit from it

## Slide 32: Coding hints
Don’t write a plugin from scratch
  use an existing one as code base
  choose one which is technically similar
    input? output? PSI/SI transformation? packet filtering?
Implement simple & elementary features
  preserve TSDuck philosophy
    develop several elementary plugins if necessary
    not a single big plugin implementing several features
RTFM as usual !

## Slide 33: Supported environments
Linux
  tested on Intel 32 & 64 bits (Fedora, Ubuntu), ARM 32 bits (Raspberry Pi)
macOS
  tested on macOS High Sierra 10.13
Windows
  tested on Intel 32 & 64 bits, Windows 7 & 10
  Microsoft Visual Studio 2017 Community Edition
    free download from microsoft.com, no license fee
  NSIS (Nullsoft Scriptable Install System)
    free software,
    used to create TSDuck installer with precompiled binaries

## Slide 34: to develop third-party applications
Using TSDuck Library

## Slide 35: The TSDuck library
All TSDuck common code is in one large library
  tsduck.so / tsduck.dll
Contains generic and reusable C++ code
  basic operating system independent features
    system, multi-treading, synchronization, networking, cryptography, etc.
  MPEG / DVB features
    TS packets, PSI/SI tables, sections and descriptors, demultiplexing, packetization, DVB tuners, etc.
Can be used in your application
  even if not part of TSDuck

## Slide 36: Using TSDuck as a library
Used in an application outside TSDuck
Install the TSDuck development environment
  Windows: “Development” option in installer
  Ubuntu, Debian, Raspbian: package tsduck-dev
  Fedora, Red Hat, CentOS: package tsduck-devel
Typical application source file
    #include "tsduck.h"
    ... application code ...

## Slide 37: Building with TSDuck library on UNIX
Typical Linux Makefile
    include /usr/include/tsduck/tsduck.mk
    ... application-specific rules ...
Typical macOS Makefile
    include /usr/local/include/tsduck/tsduck.mk
    ... application-specific rules ...

## Slide 38: Building with TSDuck library on Windows
Use Microsoft Visual Studio 2017
  Community Edition is free
Modify the application’s project file (app.vcxproj)
  Add one reference to the TSDuck property file
    <Import Project="$(TSDUCK)\tsduck.props" />
  Just before the final </Project> closing tag
  And build the application as usual

## Slide 39: Thank you