## Slide 1: TSDuck
an extensible toolkit for
MPEG/DVB transport streams
TSDuck Version 3.1

## Slide 2: Agenda
TSDuck overview
TS utilities
Transport stream processor
Extending TSDuck
Using TSDuck as an MPEG/DVB library for C++

## Slide 3: TSDuck overview
Process ISO/IEC 13818-1 transport streams
Set of low-level utilities
  extensible through plugins
« Batch & Bash » oriented
  command-line only, no fancy GUI
  one utility or plugin = one elementary function
  can be combined in any order
Written in C++
  reusable and extensible code
Available on Linux, Windows and macOS

## Slide 4: TSDuck sample usages
TS acquisition (satellite, terrestrial, IP, etc.)
TS analysis
Transmodulation
Injection of PSI / SI
TS packets carousel generation
  packetization of SSU, etc.
Test bed for CAS or STB
  injection of test cases
  DVB Scrambling and DVB SimulCrypt support
Any combination of the above and more…

## Slide 5: TSDuck availability
Open source code
    https://github.com/tsduck/tsduck
BSD license
  liberal, no GPL-like contamination
Binary installers
  for Windows, Fedora, Ubuntu

## Slide 6: TSDuck documentation
User’s Guide
    https://github.com/tsduck/tsduck/raw/master/doc/tsduck.pdf
  utilities reference
  tsp plugins reference
  sample usages
Programmer’s Reference
    https://tsduck.github.io/
  generated by Doxygen from source code
  C++ common code reference
  writing tsp plugins guidelines

## Slide 7: the command line utilities summary
TS Utilities

## Slide 8: TS utilities : data & devices
Transport stream file
  raw binary file, sequence of 188-byte TS packets
    use tsresync to convert 204-byte packets or corrupted files
  by default, use standard input & output
    can use pipes from / to any DVB source
PSI / SI file
  raw binary file, sequence of sections
Specialized hardware
  DVB-S, DVB-T, DVB-C tuners (cheap CE devices)
  Dektec modulators and ASI input / output (PCI, USB)
  smartcards
  on Linux and Windows but not macOS

## Slide 9: TS utilities summary (1/4)
Transport stream processor
  tsp : processing framework using plugins
TS analysis
  tsanalyze : synthetic report
    TS structure, services, PID’s
    can also produce a « normalized » output for automatic processing
  tspsi : detailed analysis of main PSI / SI tables in TS
    PAT, CAT, PMT, SDT, NIT, BAT
  tsbitrate : evaluate original bitrate from PCR’s
  tsdate : extract date & time information

## Slide 10: TS utilities summary (2/4)
Transport packet analysis
  tsdump : dump and analyze transport packets
TS files recovery
  tsresync : fix corrupted capture files
  tsftrunc : truncate TS files
  tsfixcc : fix continuity counters

## Slide 11: TS utilities summary (3/4)
PSI / SI tables
  tstables : extract sections & tables from TS
    either binary or textual analysis
  tstabdump : textual analysis of binary table files
  tspacketize : generate TS packets from tables
    sample usage : delivery of packet carousel for tables
  tsgentab : generate specific tables using plugins
    each plugin typically generates one table
    add new plugins when new tables are needed

## Slide 12: TS utilities summary (4/4)
Various DVB hardware support
  tsdektec : control Dektec devices
  tslsdvb : list DVB receiver devices
  tsscan : scan frequencies in a DVB network
  tsterinfo : compute various DVB-T information
  tssmartcard : list or reset smartcard reader devices

## Slide 13: the transport stream processor
TSP

## Slide 14: TSP overview
Transport stream processing framework
  Combination of elementary processing using plugins
  One input plugin
    receive a TS from various sources
  Any number of packet processing plugins
    perform transformations on TS packets
    may remove packets
    may NOT add packets
  One output plugin
    send the resulting TS to various destinations

## Slide 15: TSP processing overview
tsp process
tsp executable
packet processing plugin 2
packet processing plugin 1
packet processing plugin 3
input plugin
output plugin
input TS
output TS

## Slide 16: TSP plugins
Each tsp plugin is a shareable library
  .so file on Linux and macOS
  .dll file on Windows
File naming
  plugin named foo in file tsplugin_foo.so (or .dll)
  same directory as tsp executable
General command line syntax
  tsp [tsp-options] [-I input-name [input-options]] [-P processor-name [processor-options]] ... [-O output-name [output-options]]

## Slide 17: TSP examples (1/4)
TS acquisition
  tsp –I dvb –-uhf 21 -P until –-seconds 20 -O file capture.ts
Display the PMT of a selected service
  tsp –I dvb –-uhf 35 -P zap france2 -P sifilter –-pmt -P tables –-max 1 -O drop
capture DVB-T stream from UHF channel 21
pass packets during 20 seconds, then stop
save TS to file capture.ts
extract service « France 2 », rebuild SPTS
extract PID containing PMT
display one table, then stop
drop output packet (don’t care)

## Slide 18: TSP examples (2/4)
Transmodulation of a service over IP multicast
  tsp –I dvb –-uhf 35 -P zap france2 –-audio fra -O ip 224.10.11.12:1000
On-the-fly replacement of a PSI / SI table
  tsp -I dvb --uhf 24 -P inject nit.bin --pid 16 --replace –-stuffing -O dektec --uhf 24 --convolution 2/3 --guard 1/32
extract service « France 2 », keeping only one audio track
broadcast resulting SPTS to multicast IP address:port
replace content of PID 16 with table from binary file
send modified TS to a Dektec DVB-T modulator on same frequency

## Slide 19: TSP examples (3/4)
Conditional Access System test bed
  example using French DVB-T network
Linux or Windows computer
ECMG
EMMG
STB
UHF
coupler
UHF
antenna
MUX: R1, R2, R3, R4, R5, R6
MUX: R9
tsp
DVB-T
tuner
Dektec
DTA-110T
modulator

## Slide 20: TSP examples (4/4)
Conditional Access System test bed (continued)
  tsp -I dvb -u $UHF_INPUT
  -P tsrename -t 9 -a
  -P svrename direct8 -i 0x0901 -l 41 -n "Direct 8 Test"
  -P svrename bfmtv -i 0x0903 -l 42 -n "BFM TV Test"
  -P svrename 'i>tele' -i 0x0904 -l 43 -n "i>TELE Test"
  -P svrename virgin17 -i 0x0905 -l 44 -n "Virgin 17 Test"
  -P svrename gulli -i 0x0906 -l 45 -n "Gulli Test"
  -P svrename france4 -i 0x0907 -l 46 -n "France 4 Test"
  -P svrename 0x02FF -i 0x09FF
  -P scrambler GulliTest -e $ECMG -s $SUPER_CAS_ID
  -p $PMT_CADESC_PRIVATE -a $AC
  -b $ECM_BITRATE --pid $ECM_PID
  -P cat -c -a $CAS_ID/$EMM_PID/$CAT_CADESC_PRIVATE
  -P datainject -r -s $MUX_SERVER_PORT
  -b $EMM_MAX_BITRATE -p $EMM_PID
  -O dektec -u $UHF_OUTPUT --convolution 2/3 --guard 1/32

## Slide 21: TSP input & output plugins
Input plugins
  null : null packet generator
  file : binary TS file
  dektec : Dektec ASI device
  dvb : DVB-S, DVB-T, DVB-C receiver devices
  ip : UDP/IP (unicast or multicast)
Output plugins
  drop : drop packets
  file : binary TS file
  dektec : Dektec ASI or modulator device
  ip : UDP/IP (unicast or multicast)

## Slide 22: TSP processing plugins
TS transformations
  PID or packet filtering, PSI/SI transformation or injection, service extraction, time regulation, etc.
TS analysis and monitoring
  TS analysis, PSI/SI extraction, PID, bitrate monitoring, ECM or EMM monitoring, etc.
TS scrambling & descrambling
  DVB SimulCrypt support for ECM / EMM injection
Any other processing you wish to develop…

## Slide 23: C++ transport stream programming
Extending TSDuck

## Slide 24: Extending TSDuck
TSDuck is extensible
  Source code provided
      git clone https://github.com/tsduck/tsduck.git
  Common API for Linux, Windows and macOS
    DVB tuners and Dektec cards are not supported on macOS
  Programmer’s guide
    Doxygen-generated
      https://tsduck.github.io/
You can modify it yourself !

## Slide 25: Why extending TSDuck ?
Identify your needs
Try to find a solution using existing TSDuck
  review utilities and plugins
Try to extend an existing utility or plugin
  add new options
  add features, don’t modify existing behavior
  remain upward compatible
Develop your own plugin
  it is quite simple, really
Send your code back to TSDuck maintainer
  so that everyone can benefit from it

## Slide 26: Coding hints
Don’t write a plugin from scratch
  use an existing one as code base
  choose one which is technically similar
    input? output? PSI/SI transformation? packet filtering?
Implement simple & elementary features
  preserve TSDuck philosophy
    develop several elementary plugins if necessary
    not a single big plugin implementing several features
RTFM as usual !

## Slide 27: Supported environments
Linux
  tested on Intel 32 & 64 bits, Fedora and Ubuntu
macOS
  tested on macOS Sierra 10.12
Windows
  tested on Intel 32 & 64 bits, Windows 7 & 10
    on 64-bit Windows, use 32-bit TSDuck if your DVB tuner driver is 32-bit only
  Microsoft Visual Studio 2017 Community Edition
    free download from microsoft.com, no license fee
  NSIS (Nullsoft Scriptable Install System)
    free software
    used to create TSDuck installer with precompiled binaries

## Slide 28: to develop third-party applications
Using TSDuck Library

## Slide 29: Using TSDuck as a library (1/2)
All TSDuck common code is in one large library
  tsduck.so / tsduck.dll
Contains generic and reusable C++ code
  basic operating system independent features
    system, multi-treading, synchronization, networking, cryptography, etc.
  MPEG / DVB features
    TS packets, PSI/SI tables, sections and descriptors, demultiplexing, packetization, DVB tuners, etc.
Can be used in your application
  even if not part of TSDuck

## Slide 30: Using TSDuck as a library (2/2)
Used in an application outside TSDuck
Typical Makefile (Linux, macOS)
    # Include TSDuck makefile (adapt to your location)
    include $(HOME)/tsduck/Makefile.tsduck
    default: myexec
    myexec: $(LIBTSDUCK)
    ... application-specific rules ...
Typical application source file
    #include "tsduck.h"
    ... application code ...

## Slide 31: Thank you