## Slide 1: TSDuck
an extensible toolkit for
MPEG/DVB transport streams
https://tsduck.io

## Slide 2: What is TSDuck ?
A general-purpose toolbox for digital TV engineers
Working on MPEG transport streams
  Broadcast and IP-TV (but not OTT)
Flexible and extensible
Lots of small tools and plugins to be combined
Command line only, no GUI
Made for scripting
Available on Linux, Windows and macOS

## Slide 3: TSDuck use cases
Digital television systems
  test
  demo
  network monitoring
  system integration
  debug
  lab

## Slide 4: TSDuck sample usages
Acquisition or transmodulation : satellite, terrestrial, IP …
Analysis : TS, PSI/SI, bitrates, timestamps …
Monitoring : bitrates, A/V properties, signalization, crypto …
On-the-fly transformation or injection : content, PSI/SI …
Using and editing PSI/SI in XML or binary format
Modify, remove, rename, extract services
Inject or extract MPE, SCTE 35 splicing info
Extract T2-MI, Teletext subtitles
Test bed for CAS or STB, scrambling and DVB SimulCrypt

## Slide 5: TSDuck input / output
Live transport stream or offline files equally
UDP/IP, HTTP
Specialized hardware
  cheap DVB tuners (USB, PCI)
  professional Dektec devices
  cheap HiDes modulators
Re-route transport streams to / from other applications

## Slide 6: TSP – the transport stream processor
Transport stream processing framework
  combination of elementary processing using plugins
    60+ standard plugins available
  one input plugin
    receive a TS from various sources
  any number of packet processing plugins
    perform transformations on TS packets
    may remove packets
    may NOT add packets
  one output plugin
    send the resulting TS to various destinations

## Slide 7: TSP processing overview
tsp process
tsp executable
packet processing plugin 2
packet processing plugin 1
packet processing plugin 3
input plugin
output plugin
input TS
output TS

## Slide 8: Sample MPE injection and extraction
MPE : Multi-Protocol Encapsulation
Media Server
Network 1
Linux or Windows
DVB
tuner
Linux or Windows
Dektec modulator
STB
STB
Multicast to
224.250.250.1 : 9000
Network 2
STB
STB
Multicast to
230.2.3.4 : 7000
STB
MPE encapsulation
inside existing TS
DVB
tuner
tsp
Modified destination
in UDP/IP datagrams:
230.2.3.4 : 7000
tsp

## Slide 9: Multiple TSP using merge and fork plugins
Merge with a TS coming from another application
  merge service references (PAT, CAT, SDT …)
Duplicate the TS to another application
tsp
input
input TS 2
output TS 2
plugin
merge
merge
plugin
fork
fork
output
tsp
input
plugin
plugin
file
tsp
input
plugin
plugin
file
input TS 1
input TS 3
tsp
file
plugin
plugin
output
tsp
file
plugin
plugin
output
output TS 1
output TS 3

## Slide 10: Conditional Access System test bed
DVB SimulCrypt interface to standard CAS equipment
sample setup using French DVB-T network
Linux or Windows computer
ECMG
EMMG
STB
UHF
coupler
UHF
antenna
MUX: R1, R2, R3, R4, R5, R6
MUX: R9
tsp
DVB-T
tuner
Dektec
DTA-110T
modulator

## Slide 11: Simple TSP examples
Transmodulation of a service over IP multicast
  tsp –I dvb –-uhf 35 -P zap france2 –-audio fra -O ip 224.10.11.12:1000
On-the-fly replacement of a PSI / SI table
  tsp -I dvb --uhf 24 -P inject nit.xml --pid 16 --replace –-stuffing -O dektec --uhf 24 --convolution 2/3 --guard 1/32
extract service « France 2 », keeping only one audio track
broadcast resulting SPTS to multicast IP address:port
replace content of PID 16 with table from XML file
send modified TS to a Dektec DVB-T modulator on same frequency

## Slide 12: TSDuck utilities
TSP – transport stream processor
PSI/SI  XML compiler / decompiler
PSI/SI manipulation, extraction, injection
Analysis tools
TS files manipulation and recovery
Hardware devices configuration (tuners, modulators …)

## Slide 13: TSDuck is extensible
Open source
    https://github.com/tsduck/tsduck
Design based on a large TSDuck library
  generic MPEG/DVB C++ library (400+ classes)
  common API for Linux, Windows and macOS
  programmer’s guide online
You may use this library to
  develop new plugins
  use in your own applications outside TSDuck

## Slide 14: https://tsduck.io/